## Slide 1: LORA Protocol
Summary and analysis

## Slide 2: Basic LORA Principle
  LORA is a long-range, low power radio-communication modulation protocol
  The protocol is based on the spread spectrum technique utilizing a combination of ‘up’ and ‘down’ chirps across the available frequency bandwidth. Every LORA transmission begins with 10 up chirps and 2 down chirps followed by the encoded signal.
  Transmission occurs on the license free regional ISM band (EU863-870 or EU433)
  Signal interference with the transmission signal is non-existent as each signal component is on a different frequency resulting in no conflict

## Slide 3: LORA Parameters
  Symbol: Refers to the actual/unencoded value intended on being transmitted, one or more symbols makes a signal
  Symbol Duration: Refers to the time utilized in the transmission signal for each modulated symbol
  Spreading Factor: SF sets the number of chirps for the carriers signal that are sent per second and can be set between 7 - 12
  Bandwidth: This is the minimum and maximum frequency available for transmission centered around the carrier ISM frequency or more generally number of wave cycles per second
  Transmission Power: The refers to the [db] power gain at the transmitted that affects the range and ability to propagate through obstacles for the modulated signal
  Coding Rate: The process of adding error correction bits to the signal in the event of signal interference

## Slide 4: Parameter Relationships
There are three main initial parameters that can be set. These magnitude of each parameter has various consequences affecting transmission signal.
The parameters are:
  Spreading Factor
  Bandwidth
  Transmission Power
  Note the coding rate also does affect the data rate with more bits needed to be transmitted and thus more power used but better error correction

## Slide 5: Spreading Factor:
  Increase the Spreading Factor results in:
  - Decrease in data rate
  - Symbol duration increases
  - Transmission time increases ( More susceptible to collisions)
  - Increase in number of symbol raw bits equivalent to SF magnitude
  The number of chips generated for modulation is 2^(SF) for each symbol
  Higher spreading factor == greater range but utilizes more power
  == weaker transmission signals

## Slide 6: Bandwidth and Transmission Power:
  Increase in Bandwidth results in:
  - Increase in data rate
  - Symbol duration decreases
  - Transmission time decreases
With an increase in the transmission power:
    Signals are more susceptible to collisions and obstacles
    Can travel further
    Trade-off – utilize more power

## Slide 7: Ideal Optimal Parameters
Optimisation Goals
Minimal battery use
Maximum transmission range
Obstacle/collision mitigation
Minimal error rate
Ideal parameters
Lower SF, reduced data-rate, less signal power
Higher SF, longer transmission times, more signal power, smaller bandwidth
Increased transmission time, Higher spreading factor
Greater bandwidth and higher coding rate

## Slide 8: Realistic Optimal Parameters
Given that the radiosonde has the ability to measure the current location and thus the distance between the ground receiver and lora client, an adaptive approach can be taken:
The battery on the client realistically only has to last for a few hours (about 4 – 6 hours) thus less importance can be assigned to battery usage. Tx power can thus be increased , the further the client is from the ground receiver
Most importance assigned. The SF can initial be set to 7 and then increased as the distance increases so can the SF to achieve better range repeat with BW except begin at a higher BW
Line of sight should be achievable relatively easily and hence less importance assigned but will be improved base on 2 as at longer ranges the SF will be increased
Error correction is important but increasing the coding rate and this the band width would conflict with the range and thus realistically only a minimal coding rate would be used