## Slide 1: LoRa Project Update
Done by:
Yashiv Fakir

## Slide 2: Initial Project Specifications
Project Outline
Utilize pre built LoRa modules to develop a communication method for radiosonde data, for weather balloon applications. This is to be done between the modules. Overall, to establish if the protocol can be used for this application.
Beginning with land tests and ending with a balloon test.
Aspects Required to be Met
- Bandwidth: 1200 – 4800 bps
- Range: 100 km
- Altitude: 35 – 38 km
- Temperature: Environment temp = -90 C
- Explore effect of balloon tracking
- Explore effect data compression algorithms

## Slide 3: Current Project Specifications
Project Outline
Similar to initial specifications excluding the effect of temperature and an actual weather balloon test.
The main focus shifted to optimizing the LoRa parameters to maximise range as quickly established that LoRa can be used for this application already.
Aspects being met
- Bandwidth: 1200 – 4800 bps
- Range: 1.2 km (but can be propagated to get theoretical max distance
- Altitude: +- 100 m (Wind preventing max height)
- Drone tracking from ground
- Data compression using real data

## Slide 4: Project Components that are Completed
Parameters for the protocol have been tested and results taken for:
  BW, Carrier Frequency, Spreading Factor, Coding Rate
  Output in terms of RSSI values showing success for smaller BW and carrier frequency. The spreading factor however is not reflecting a clear winner shown to the right.
  Have established optimal LoRa parameters with the exception of SF
  Have acquired some real life radiosonde data and begun exploring compression/encoding methods

## Slide 5: Project Components that are Completed Continued
Both LoRa modules of 433 MHz and 868 MHz have been coded and work
The GPS module required for the stand is coded (but cannot calculate elevation)

## Slide 6: Project Components that still need to be Completed
Tasks that still need to be done:
  Explore and code data compression algorithms
  Perform a range test with compressed radiosonde data
  Perform a mountain to mountain long range test
  Perform a drone tracking test using the stand
  Stand is almost complete and can be printed, just waiting for the dimensions of the motors to model a socket for the motors
  Develop code to govern the two stepper motors
  Continue writing the report